## Slide 1
XI. Hilbert Huang Transform (HHT)
Proposed by 黃鍔院士 (AD. 1998)
[1] N. E. Huang, Z. Shen, S. R. Long, M. C. Wu, H. H. Shih, Q. Zheng, N. C. Yen, C. C. Tung, and H. H. Liu, “The empirical mode decomposition and the Hilbert spectrum for nonlinear and non-stationary time series analysis,” Proc. R. Soc. Lond. A, vol. 454, pp. 903-995, 1998.
[2] N. E. Huang and S. Shen, Hilbert-Huang Transform and Its Applications, World Scientific, Singapore, 2005.
References
http://djj.ee.ntu.edu.tw/%E9%BB%83%E9%8D%94%E9%99%A2%E5%A3%AB.pdf
黃鍔院士的生平可參考
(PS: 謝謝 2007 年修課的趙逸群同學和王文阜同學)

## Slide 2
11-A The Origin of the Concept
另一種分析 instantaneous frequency 的方式： Hilbert transform
 Hilbert transform
or
H(f)
f-axis
-j
j
f = 0

## Slide 3
 analytic signal
 another way to define the instantaneous frequency:
where
Example:
Applications of the Hilbert Transform
 edge detection

## Slide 4
Problem of using Hilbert transforms to determine the instantaneous frequency:
This method is only good for cosine and sine functions with single component.
Not suitable for (1) complex function
(2) non-sinusoid-like function
(3) multiple components
Example:
Moreover, (4)  has multiple solutions.

## Slide 5
 Hilbert-Huang transform 的基本精神：
先將一個信號分成多個 sinusoid-like components + trend
(和 Fourier analysis 不同的地方在於，這些 sinusoid-like components 的 period 和 amplitude 可以不是固定的)
再運用 Hilbert transform (或 STFT，number of zero crossings) 來分析每個 components 的 instantaneous frequency
完全不需用到 Fourier transform

## Slide 6
11-B Intrinsic Mode Function (IMF)
但要滿足
(1) The number of extremes and the number of zero-crossings must either equal or differ at most by one.
(2) At any point, the mean value of the envelope defined by the local maxima and the envelope defined by the local minima is near to zero.
local maximums & local minimums
Amplitude and frequency can vary with time.

## Slide 7
11-C Procedure of the Hilbert Huang Transform
(Step 2) Find the local peaks
-1
0
1
2
Steps 1~8 are called Empirical Mode Decomposition (EMD)
y(t)
(Step 1) Initial: y(t) = x(t), (x(t) is the input) n = 1, k = 1

## Slide 8
(Step 3) Connect local peaks
-1
0
1
2
IMF 1; iteration 0
通常使用 B-spline，尤其是 cubic B-spline 來連接
(參考附錄十一)

## Slide 9
(Step 4) Find the local dips
(Step 5) Connect the local dips
-1
0
1
2
IMF 1; iteration 0

## Slide 10
(Step 6-1) Compute the mean
-1
0
1
2
IMF 1; iteration 0
(pink line)

## Slide 11
(Step 6-2) Compute the residue
-1.5
-1
-0.5
0
0.5
1
1.5

## Slide 12
(Step 7) Check whether hk(t) is an intrinsic mode function (IMF)
If not, set y(t) = hk(t), k = k + 1, and repeat Steps 2~6
If they are satisfied (or k ≧ K), set cn(t) = hk(t) and continue to Step 8
cn(t) is the nth IMF of x(t).
(2) 上封包： u1(t)， 下封包： u0(t)
(1) 檢查是否 local maximums 皆大於 0
local minimums 皆小於 0
檢查是否
for all t
(為了避免無止盡的迴圈，可以定 k 的上限 K)

## Slide 13
(Step 8) Calculate
and check whether x0(t) is a function with no more than one extreme point.
If not, set n = n+1, y(t) = x0(t)
and repeat Steps 2~7
If so, the empirical mode decomposition is completed.
Step 1
Steps 2~6
hk(t) is an IMF?
N
Yes
x0(t) has only 0~3 extreme?
Yes
No
Step 7
Step 8
Step 9
trend
Set
y(t) = x(t)
y(t) = hk(t)
y(t) = x0(t)
n=0
n = n+1

## Slide 14
(Step 9) Find the instantaneous frequency for each IMF cs(t) (s = 1, 2, …, n).
Method 1: Using the Hilbert transform
Method 2: Calculating the STFT for cs(t).
Method 3: Furthermore, we can also calculate the instantaneous frequency from the number of zero-crossings directly.
instantaneous frequency Fs(t) of cs(t)

## Slide 15
(A) 邊界處理的問題：
目前尚未有一致的方法，可行的方式有
(1) 只使用非邊界的 extreme points
(2) 將最左、最右的點當成是 extreme points
(3) 預測邊界之外的 extreme points 的位置和大小
(4) 用邊界和最近的 extreme point 的距離來判斷是否邊界要當成 extreme points
(B) Noise 的問題：
先用 pre-filter 來處理
Technique Problems of the Hilbert Huang Transform

## Slide 16
最左、最右的點是否要當成是 extreme points

## Slide 17
11-D Example
Example 1
After Step 6

## Slide 18
IMF1
IMF2
x0(t)

## Slide 19
hum signal
IMF1
IMF2
Example 2

## Slide 20
IMF3
IMF4
IMF5
IMF6

## Slide 21
IMF7
IMF8
IMF9
IMF10

## Slide 22
IMF11
x0(t)

## Slide 23
11-E Comparison
(1) 避免了複雜的數學理論分析
(2) 可以找到一個 function 的「趨勢」
(3) 和其他的時頻分析一樣，可以分析頻率會隨著時間而改變的信號
(4) 適合於 Climate analysis
Economical data
Geology
Acoustics
Music signal

## Slide 24
 Conclusion
當信號含有「趨勢」
或是由少數幾個 sinusoid functions 所組合而成，而且這些sinusoid functions 的 amplitudes 相差懸殊時，可以用 HHT 來分析

## Slide 25
附錄十一 Interpolation and the B-Spline
Suppose that the sampling points are t1, t2, t3, …, tN and we have known the values of x(t) at these sampling points.
There are several ways for interpolation.
(1) The simplest way: Using the straight lines (i.e., linear interpolation)
t1
t2
t3
t4

## Slide 26
(2) Lagrange interpolation
 指的是連乘符號，
Example: When N = 4,

## Slide 27
(3) Polynomial interpolation
solve a1, a2, a3, ……, aN-1 from

## Slide 28
(4) Lowpass Filter Interpolation
適用於 sampling interval 為固定的情形 tn+1  tn = t for all n
x(tn)
discrete time Fourier transform
X1(f)
lowpass mask
X (f)
inverse discrete time Fourier transform
x(t)

## Slide 29
for tn < t < tn+1
otherwise
m = 1: linear B-spline
m = 2: quadratic B-spline
m = 3: cubic B-spline (通常使用)
B-spline 簡稱為 spline
(5) B-Spline Interpolation
are continuous
for tn < t < tn+m+1

## Slide 30
In Matlab，the command“spline” can be used for spline interpolation.
(Note： In the command, the cubic B-spline is used)
Cubic B-Spline Interpolation by Matlab:
Generating a sine-like spline curve and samples it over a finer mesh:
x = 0:1:10; % original sampling points
y = sin(x);
xx = 0:0.1:10; % new sampling points
yy = spline(x,y,xx);
plot(x,y,'o',xx,yy)

## Slide 31
事前安裝模組
pip install numpy
pip install scipy
pip install matplotlib
Reference : https://docs.scipy.org/doc/scipy/reference/reference/generated/scipy.interpolate.interp1d.html#scipy.interpolate.interp1d
In Python, we can use the following way to perform cubic B-spline interpolation.
感謝2021年擔任助教的蔡昌廷同學

## Slide 32
Cubic B-Spline Interpolation by Python
from scipy.interpolate import interp1d
import matplotlib.pyplot as plt
import numpy as np
x = np.arange(0, 11) # original sample points, [0, 1, 2, …, 9, 10]
y = np.sin(x)
f = interp1d(x, y, kind=' cubic ') ) # Cubic means the cubic B-spline.
x_new = np.arange(0, 10.1, 0.1)
# new sample points, [0, 0.1, 0.2, ….., 9.9, 10]
y_new = f(x_new)
plt.plot(x,y,'o',x_new, y_new)
plt.show()