## Slide 1: II. Short-time Fourier Transform
Short-time Fourier transform (STFT)
Alternative definition
[1] S. Qian and D. Chen, Section 3-1 in Joint Time-Frequency Analysis: Methods and Applications, Prentice-Hall, 1996.
[2] S. H. Nawab and T. F. Quatieri, “Short time Fourier transform,” in Advanced Topics in Signal Processing, pp. 289-337, Prentice Hall, 1987.
參考資料
II-A Definition

## Slide 2
Inverse of the STFT: To recover x(t),
where w(t1 – t)  0.
For the alternative definition, the inverse transform is:
STFT

## Slide 3
The mask function w(t) always has the property of
(a) even: w(t) = w(t), (通常要求這個條件要滿足)
(b) max(w(t)) = w(0), w(t1)  w(t2) if |t2| > |t1|
(c) w(t)  0 when |t| is large
w(t) = (t) (triangular function) w(t) = exp(a|t|b)
Max[(t)] = 1
t =  1 t = 1
(hyper-Laplacian function)

## Slide 4
Rectangular mask STFT (rec-STFT)
Inverse of the rec-STFT
where t – B < t1 < t + B
The simplest form of the STFT
Other types of the STFT may require more computation time than the rec-STFT.
II-B Rec-STFT
-B B
t-axis
0

## Slide 5
II-C Properties of the Rec-STFT
(1) Integration (recovery):
(a) when v B < t < v + B,
= 0 otherwise
(b)

## Slide 6
(2) Shifting property (橫的方向移動)
(3) Modulation property (縱的方向移動)

## Slide 7
(4) Special inputs:
(1) When x(t) = (t),
when –B < t < B, otherwise
(2) When x(t) = 1
思考： B 值的大小，對解析度的影響是什麼？

## Slide 8
(5) Linearity property
If h(t) =  x(t) +  y(t) and H(t, f ), X(t, f ) and Y(t, f ) are their rec-STFTs, then
H(t, f ) =  X(t, f ) +  Y(t, f ).
(6) Power integration property
(7) Energy sum property (Parseval’s theorem)

## Slide 9
思考:
(1) 哪些性質 Fourier transform 也有？
(2) 其他型態的 STFT 是否有類似的性質？
Shifting
Modulation

## Slide 10
Example: x(t) = cos(2 t) when t < 10,
x(t) = cos(6 t) when 10  t < 20,
x(t) = cos(4 t) when t  20

## Slide 12
All the time-frequency analysis methods has the advantage of:
The instantaneous frequency can be observed.
All the time-frequency analysis methods has the disadvantage of:
Higher complexity for computation
II-D Advantage and Disadvantage
 Compared with the Fourier transform:

## Slide 13
 Compared with other types of time-frequency analysis:
The rec-STFT has an advantage of the least computation time for digital implementation
but its performance is worse than other types of time-frequency analysis.

## Slide 14
II-E STFT with Other Windows
(1) Rectangle
(2) Triangle
(3) Hanning
(4) Hamming
(5) Gaussian
-2B 2B
-B B

## Slide 15
(6) Asymmetric window
 = 0
-axis
應用： seismic wave analysis, collision detection
(The applications that require real-time processing)
-B1
B2
B1 < B2
w()
w(t-) = ?

## Slide 16
動腦思考：
Are there other ways to choose the mask of the STFT?
Which mask is better?
沒有一定的答案

## Slide 17
II-F Spectrogram
STFT 的絕對值平方，被稱作 Spectrogram
文獻上，spectrogram 這個名詞出現的頻率多於 STFT
但實際上， spectrogram 和 STFT 的本質是相同的
比較： spectrum 為 Fourier transform 的絕對值平方

## Slide 18
附錄三：使用 Matlab 將時頻分析結果 Show 出來
可採行兩種方式：
(1) 使用 mesh 指令畫出立體圖
(但結果不一定清楚，且執行時間較久)
(2) 將 amplitude 變為 gray-level，用顯示灰階圖的方法將結果表現出來
假設 y 是時頻分析計算的結果
image(abs(y)/max(max(abs(y)))*C) % C 是一個常數，我習慣選 C=400
或 image(t, f, abs(y)/max(max(abs(y)))*C)
colormap(gray(256)) % 變成 gray-level 的圖
set(gca,‘Ydir’,‘normal’) % 若沒這一行, y-axis 的方向是倒過來的

## Slide 19
計算程式執行時間的指令：
tic (這指令如同按下碼錶)
toc (show 出碼錶按下後已經執行了多少時間)
註：通常程式執行第一次時，由於要做程式的編譯，所得出的執行時間會比較長
程式執行第二次以後所得出的執行時間，是較為正確的結果
set(gca,‘Fontsize’,12) % 改變橫縱軸數值的 font sizes
xlabel('Time (Sec)','Fontsize',12) % x-axis
ylabel('Frequency (Hz)','Fontsize',12) % y-axis
title(‘STFT of x(t)','Fontsize',12) % title

## Slide 20
附錄四：使用 Python 將時頻分析的圖畫出來
事前安裝模組
pip install numpy
pip install matplotlib
假設y為時頻分析結果(應為二維的矩陣數列)，將 y 以灰階方式畫出來
import numpy as np
import matplotlib.pyplot as plt
C = 400
y = np.abs(y) / np.max(np.abs(y)) * C
plt.imshow(y, cmap='gray', origin='lower')
# 加上 origin='lower' 避免上下相反
plt.xlabel('Time (Sec)')
plt.ylabel('Frequency (Hz)')
plt.show()
感謝2021年擔任助教的蔡昌廷同學

## Slide 21
若要加上座標軸數值(在plt.show()之前加上以下程式碼)
x_label = [‘0’, ‘10’, ‘20’, ‘30’] # 橫軸座標值
y_label = [‘-5’, ‘0’, ‘5’] # 縱軸座標值
plt.xticks(np.arange(0, x_max, step=int(x_max/(len(x_label)-1)), x_label)
plt.yticks(np.arange(0, y_max, step=int(y_max/(len(y_label)-1)), y_label)
Reference : https://matplotlib.org/stable/api/_as_gen/matplotlib.pyplot.xticks.html