## Slide 1: IX. Basic Implementation Techniques and Fast Algorithm
344
Fast Algorithm Design
Goals: Saving Computational Time
Number of Additions
Number of Multiplications
Number of Time Cycles
Saving the Hardware Cost for Implementation
Saving the buffer size
Repeated Using a Structure
 9-A 快速演算法設計的原則

## Slide 2
345
Four important concepts that should be learned from fast algorithm design:
(1) N-point DFT
(2) Complexity of LTI Systems
(3) Replacement of DFTs
(4) Simplification Techniques

## Slide 3
如何簡化下面四個運算
y1 = ax1 + 2ax2
346
 9-B 對於簡單矩陣快速演算法的設計

## Slide 4
(i) z1 = a[x1 + x2], z2 = z1
(ii) z3 = (b−a)x2, z4 = (c−a)x1
(iii) y1 = z1 + z3, y2 = z2 + z4
347
(4)

## Slide 5
問題思考：如何對 complex number multiplication 來做 implementation？

## Slide 6
 9-C General Way for Simplifying Calculation
假設一個 MN sub-rectangular matrix S 可分解為 column vector 及 row vector 相乘
若 [a1, a2, …., aM]T 有 M0 個相異的 non-trivial values
(am  2k, am  2kah where m  h)
[b1, b2, …., bN] 有 N0 個相異的 non-trivial values
則 S 共需要 M0 + N0 個乘法
349

## Slide 7
Step 1 za = b1x[1] + b2x[2] + …. + bNx[N]
Step 2 z[1] = a1 za , z[2] = a2 za , ………, z[N] = aM za
350

## Slide 8
簡化理論的變型
S1 也是一個 MN matrix
若 S1 有 P1 個值不等於 0, 則 S 的乘法量上限為 M0 + N0 + P1
以此類推
351

## Slide 9
思考： 對於如下的情形需要多少乘法
352

## Slide 10
3  3 DFT 可以用特殊方法簡化
353
 9-D Examples
DFT:
Without any simplification, the DFT needs 4N2 real multiplications (x[n] may be complex)

## Slide 11
 5  5 DFT 的例子
354
real part
imaginary part

## Slide 12
8-point DCT
觀察對稱性質之後，令
355

## Slide 13
356
Part 1:

## Slide 14
[Ref] B. G. Lee, “A new algorithm for computing the discrete cosine transform,”
IEEE Trans. Acoust., Speech, Signal Processing, vol. 32, pp. 1243-1245, Dec. 1984.
357
Part 2:

## Slide 15
358
 N-point DFT:
 N-point DCT, DST, DHT:
 Two-dimensional (2-D) Nx  Ny-point DFT:
 Convolution of an M-point sequence and an N-point sequence:
when M/N and N/M are not large,
when N >> M and M is a fixed constant.
when M >> N and N is a fixed constant.
 9-E Summary of the Complexity
Why?

## Slide 16
359
 2-D Convolution of an (Mx  My )-point matrix and an (Nx  Ny )-point matrix:
when MxMy/NxNy and NxNy/MxMy are not large,
when MxMy >> NxNy
when NxNy >> MxMy , and Mx, My are fixed constants.

## Slide 17
 C. S. Burrus and T. W. Parks, “DFT / FFT and convolution algorithms”, John Wiley and Sons, New York, 1985.
 R. E. Blahut, Fast Algorithm for Digital Signal Processing, Addison Wesley Publishing Company.
N-point Fourier Transform: 運算量為 N2
FFT (with the Cooley Tukey algorithm): 運算量為 NlogN
X. Fast Fourier Transform
360
要學到的概念：(1)快速演算法不是只有 Cooley Tukey algorithm
(2) 不是只有 N = 2k 有時候才有快速演算法

## Slide 18
(1) Cooley-Tukey algorithm (Butterfly form)
(2) Radix-4, 8, 16, …. Algorithms
(3) Prime Factor Algorithm
(4) Goertzel Algorithm
(5) Chirp Z transform (CZT)
(6) Winograd algorithm
 10-A Other DFT Implementation Algorithms

## Slide 19
Reference
 J. W. Cooley and J. W. Tukey, “An algorithm for the machine computation of complex Fourier series,” Mathematics of Computation, vol. 19, pp. 297-301, Apr. 1965. (Cooley-Tukey)
 C. S. Burrus, “Index Mappings for multidimensional formulation of the DFT and convolution,” IEEE Trans. Acoustics, Speech, and Signal Processing, vol. 25, pp. 1239-242, June 1977. (Prime factor)
 G. Goertzel, “An algorithm for the evaluation of finite trigonometric series,” American Math. Monthly, vol. 65, pp. 34-35, Jan. 1958. (Goertzel)
 C. R. Hewes, R. W. Broderson, and D. D. Buss, “Applications of CCD and switched capacitor filter technology,” Proc. IEEE, vol. 67, no. 10, pp. 1403-1415, Oct. 1979. (CZT)
 S. Winograd, “On computing the discrete Fourier transform,” Mathematics of Computation, vol. 32, no. 141, pp. 179-199, Jan. 1978. (Winograd)
 R. E. Blahut, Fast Algorithm for Digital Signal Processing, Reading, Mass., Addison-Wesley, 1985.

## Slide 20
363
2-point DFT
g[0]
g[1]
G[0]
G[1]
-1

## Slide 21
 10-B Cooley Tukey Algorithm
When N = 2k
Therefore,
one N-point DFT = two (N/2)-point DFTs + twiddle factors
twiddle factors
x1[n] = x[2n], x2[n] = x[2n+1]
364
+
+
-1

## Slide 22
8-point DFT
x[0]
x[2]
x[4]
x[6]
x[1]
x[3]
x[5]
x[7]
4-point DFT
4-point DFT
X[0]
X[1]
X[2]
X[3]
X[4]
X[5]
X[6]
X[7]
1
w
w2
w3
-1
-1
-1
-1
365
When N = 8
twiddle factor:









## Slide 23
x[0]
x[4]
x[2]
x[6]
x[1]
x[5]
x[3]
x[7]
X[0]
X[1]
X[2]
X[3]
X[4]
X[5]
X[6]
X[7]
-1
-1
-1
-1
-1
-1
-1
-1
1
w2
1
w2
8-point DFT
1
w
w2
w3
-1
-1
-1
-1
366

## Slide 24
2k-point DFT 一共有 k 個 stages
每個 stage 和下一個 stage 之間有 2k-1 個 twiddle factors
所以，一共有 2k-1(k-1) 個 twiddle factors
一般而言，每個 twiddle factor 需要 3 個 real multiplications
 2k-point DFT 需要
 Number of real multiplications 的估算
個 real multiplications
Complexity of the N-point DFT: O(Nlog2N)
367
k-1 次 decomposition

## Slide 25
 8-point DFT 只需要 4 個 real multiplications (Why?)
 更精確的分析，使用 Cooley-Tukey algorithm 時，N-point DFT 需要
個 real multiplications
(Why?)
368

## Slide 26
 10-C Radix-4 Algorithm
限制： N = 4k
or N = 24k (此時 Cooley-Tukey algorithm 和 radix-4 algorithm 並用)
One N-point DFT = four (N/4)-point DFTs + twiddle factors
twiddle factors
369

## Slide 27
Note:
(1) radix-4 algorithm 最後可將 N = 4k-point DFT 拆解成 4-point DFTs 的組合
4-point DFTs 不需要任何的乘法
(2) 使用 radix-4 algorithm 時，N-point DFT 需要
個 real multiplications
370

## Slide 28
 Number of real multiplications for the N-point DFT
N | 乘法數 | 加法數 | N | 乘法數 | N | 乘法數 | N | 乘法數
1 | 0 | 0 | 11 | 40 | 24 | 28 | 39 | 182
2 | 0 | 4 | 12 | 8 | 25 | 148 | 40 | 100
3 | 2 | 12 | 13 | 52 | 26 | 104 | 42 | 124
4 | 0 | 16 | 14 | 32 | 27 | 114 | 44 | 160
5 | 10 | 34 | 15 | 40 | 28 | 64 | 45 | 170
6 | 4 | 36 | 16 | 20 | 30 | 80 | 48 | 92
7 | 16 | 72 | 18 | 32 | 32 | 72 | 52 | 208
8 | 4 | 52 | 20 | 40 | 33 | 142 | 54 | 228
9 | 16 | 72 | 21 | 62 | 35 | 150 | 56 | 156
10 | 20 | 88 | 22 | 80 | 36 | 64 | 60 | 160

## Slide 29
N | 乘法數 | N | 乘法數 | N | 乘法數 | N | 乘法數
63 | 256 | 96 | 280 | 192 | 752 | 360 | 1540
64 | 204 | 104 | 468 | 204 | 976 | 420 | 2080
66 | 284 | 108 | 456 | 216 | 1020 | 480 | 2360
70 | 300 | 112 | 396 | 224 | 1016 | 504 | 2300
72 | 164 | 120 | 380 | 240 | 940 | 512 | 3180
80 | 260 | 128 | 560 | 252 | 1024 | 560 | 3100
81 | 480 | 144 | 436 | 256 | 1308 | 672 | 3496
84 | 248 | 160 | 680 | 288 | 1160 | 720 | 3620
88 | 364 | 168 | 580 | 312 | 1608 | 784 | 4412
90 | 340 | 180 | 680 | 336 | 1412 | 840 | 4580

## Slide 30
N | 乘法數 | N | 乘法數 | N | 乘法數 | N | 乘法數
1008 | 5356 | 1440 | 8680 | 2520 | 16540 | 4032 | 29488
1024 | 7436 | 1680 | 10420 | 2688 | 19108 | 4096 | 37516
1152 | 7088 | 2016 | 12728 | 2880 | 20060 | 4368 | 35828
1260 | 7640 | 2048 | 16836 | 3369 | 24200 | 4608 | 36812
1344 | 8252 | 2304 | 15868 | 3920 | 29900 | 5040 | 36860

## Slide 31
374
附錄十一：量測方法的精確度常用的指標
方法判斷為真
事實上為真
TP
FN
FP
TN
TP (true positive): 事實上為真，而且被我們的方法判斷為真的情形
FN (false negative): 事實上為真，卻未我們的方法被判斷為真的情形
FP (false positive): 事實上不為真，卻被我們的方法誤判為真的情形
TN (true negative): 事實上不為真，而且被我們的方法判斷成不為真的情形

## Slide 32
375
寧可錯抓一百，也不可放過一個
recall 高，但 precision 低
寧可錯放一百，也不可冤枉一個
precision 高，但 recall 低
以抓犯人為例，TP 是有罪而且被抓到的情形，FP是無罪但被誤抓的情形，FN 是有罪但沒被抓到的情形，TN 是無罪且未被誤逮的情形
(positive prediction rate)

## Slide 33
376
F-score
General form of the F-score
Accuracy
Detection error rate