## Slide 1
2. Digital Filter Design (A)
任何可以用來去除 noise 作用的 operation，皆被稱為 filter
甚至有部分的 operation，雖然主要功用不是用來去除 noise，但是可以用 FT + multiplication + IFT 來表示，也被稱作是 filter
convolution, LTI system
=
Reference
[1] A. V. Oppenheim and R. W. Schafer, Discrete-Time Signal Processing, London: Prentice-Hall, 3rd ed., 2010.
[2] D. G. Manolakis and V. K. Ingle, Applied Digital Signal Processing, Cambridge University Press, Cambridge, UK. 2011.
[3] B. A. Shenoi, Introduction to Digital Signal Processing and Filter Design, Wiley-Interscience, N. J., 2006.
[4] A. A. Khan, Digital Signal Processing Fundamentals, Da Vinci Engineering Press, Massachusetts, 2005.
[5] S. Winder, Analog and Digital Filter Design, 2nd Ed., Amsterdam, 2002.

## Slide 2
 2-A Classification for Filters
filter
digital filter
analog filter
IIR (infinite impulse response)
FIR (finite impulse response)
bilinear transform
impulse invariant
step invariant
(1) MSE (mean square error)
(2) Minimax (minimize the maximal error)
(3) frequency sampling
others
(4) others
由設計方法分類
由 response 是否 有限長分類
由 數位類比分類
關心平均誤差
最小化最大誤差

## Slide 3
Classification for filters (依型態分)
pass-stop filter
high pass filter
all pass filter
band pass filter
band stop filter
low pass filter
Wiener filter
matched filter
equalizer filter
others
Hilbert transform
differentiation
integration
smoother
edge detection
Notch filter
0
Kalman filter
particle filter

## Slide 4
FIR filter: impulse response is nonzero at finite number of points
h[n] = 0 for n < 0 and n  N
 FIR is more popular because its impulse response is finite.
(h[n] has N points, N is a finite number)
2-B FIR Filter Design
h[n] is causal

## Slide 5
h[-1] h[0] h[1] h[k-2] h[k-1] h[k] h[k+1] h[k+2] h[N-2] h[N-1] h[N] h[N+1]
r[-k-1] r[-k] r[-k+1] r[-2] r[-1] r[0] r[1] r[2] r[k-1] r[k] r[k+1] r[k+2]
s[0] s[1]/2 s[2]/2 s[k-1]/2 s[k]/2
(a) r[n] = h[n + k], where k = (N1)/2.
Specially, when h[n] is even symmetric
h[n] = h[N−1 −n]
and N is an odd number
(b) s[0] = r[0], s[n] = 2r[n] for 0 < n  k.
(假設一)
(假設二)

## Slide 6
Impulse Response of the FIR Filter:
h[n] (h[n]  0 for 0  n  N1) r[n] = h[n + k], k = (N1)/2 (r[n]  0 for -k  n  k, see page 45)
Suppose that the filter is even, r[n] = r[n].
Set s[0] = r[0], s[n] = 2r[n] for n  0.
Then, the discrete-time Fourier transform of the filter is
(F = f t is the normalized frequency)
See page 25

## Slide 7
(1) least MSE (mean square error) form
(關心 平均 誤差)
MSE = , fs: sampling frequency
H(f): the spectrum of the filter we obtain Hd(f): the spectrum of the desired filter
(2) mini-max (minimize the maximal error) form (關心 最大 誤差)
maximal error:
The transition band is always ignored
2-C Least MSE Form and Minimax Form FIR Filters

## Slide 8
Example: desired output Hd(F)
(A) larger MSE, but smaller maximal error
(B) smaller MSE, but larger maximal error
F

## Slide 9
2-D Review: FIR Filter Design in the MSE Sense
F = f / fs

## Slide 10
From the facts that
when n  ,
when n = , n  0,
when n = , n = 0.
Therefore,
for n  0.

## Slide 11
Minimize MSE  Make for all n’s
 , .
Finally, set h[k] = s[0],
h[k+n] = s[n]/2, h[k  n] = s[n]/2 for n = 1, 2, 3, …., k,
h[n] = 0 for n < 0 and n  N.
Then, h[n] is the impulse response of the designed filter.

## Slide 12
 2-E FIR Filter Design in the Mini-Max Sense
References
[1] T. W. Parks and J. H. McClellan, “Chebychev approximation for nonrecursive digital filter with linear phase”, IEEE Trans. Circuit Theory, vol. 19, no. 2, pp. 189-194, March 1972.
[2] J. H. McClellan, T. W. Parks, and L. R. Rabiner “A computer program for designing optimum FIR linear phase digital filter”, IEEE Trans. Audio- Electroacoustics, vol. 21, no. 6, Dec. 1973.
[3] F. Mintz and B. Liu, “Practical design rules for optimum FIR bandpass digital filter”, IEEE Trans. ASSP, vol. 27, no. 2, Apr. 1979.
[4] E. Y. Remez, “General computational methods of Chebyshev approximation: The problems with linear real parameters,” AEC-TR-4491. ERDA Div. Phys. Res., 1962.
It is also called“Remez-exchange algorithm”
or “Parks-McClellan algorithm”

## Slide 13
Suppose that:
 Filter length = N, N is odd, N = 2k+1.
 Frequency response of the desired filter: Hd(F) is an even function
(F is the normalized frequency)
 The weighting function is W(F)
Two constraints

## Slide 14
用Mini-Max方法所設計出的filters，一定會滿足以下二個條件
(1) 有k+2個以上的extreme points
(2) 在extreme points上， 是定值
的情形
T. W. Parks and J. H. McClellan, “Chebychev approximation for nonrecursive digital filter with linear phase”, IEEE Trans. Circuit Theory, vol. 19, no. 2, pp. 189-194, March 1972.
證明可參考
Error 的 local maximal
local minimum
transition band

## Slide 15
Generalization for Mini-Max Sense by weight function
maximal error:
weighted maximal error:
where W(f) is the weight function.
The weight function is designed according to which band is more important.
f
passband
stopband
Hd(f)
transition band
Q: How do we choose W(f) When SNR ?

## Slide 16
Example: If we treat the passband the same important as the stopband.
W(f) = 1 in the passband, W(f) = 1 in the stopband
Q1: W(f) = 1 in the passband, W(f) < 1 in the stopband 代表什麼？
Q2: W(f) < 1 in the passband, W(f) = 1 in the stopband 代表什麼？
Q4: Weighting function 的概念可否用在 MSE sense ？
Q3: 如何用來壓縮特定區域 (如 transition band 附近) 的 error？

## Slide 17
Step1
Step2
Step5
Step3
Step4
Step6
guess Fm
s[n]
err(F)
new Fm
E1-E0
h[n]

## Slide 18
:
:
(Step 1): Choose arbitrary k+2 extreme frequencies in the range of
0  F  0.5, (denoted by F0, F1, F2, ….., Fk+1)
Note: (1) Exclude the transition band.
(2) The extreme points cannot be all in the stop band.
Set E1 (error)  
Extreme frequencies:
The locations where the error is maximal.
(參考 page 54)
 2-F Mini-Max Design Process

## Slide 19
(Step 2): From page 46, [R(Fm)  Hd(Fm)]W(Fm) = (1)m+1e (where m = 0, 1, 2, ….. , k+1) can be written as
where m = 0, 1, 2, ….. , k+1.
Expressed by the matrix form:
Solve s[0], s[1], s[2], ….. , s[k] from the above matrix
(performing the matrix inversion).
Square matrix

## Slide 20
(Step 3): Compute err(F) for 0  F  0.5, exclude the transition band.
Set W(F) = 0 at the transition band.
(Step 4): Find k+2 local maximal (or minimal) points of err(F)
local maximal point: if q() > q( + F) and q() > q(  F),
then  is a local maximal of q(x).
local minimal point: if q() < q( + F) and q() < q(  F),
then  is a local minimal of q(x).
Other rules: Page 63
Denote the local maximal (or minimal) points by
These k+2 extreme points could include the boundary points of the transition band

## Slide 21
(Step 5):
Set E0 = Max(|err(F)|).
(Case a) If E1  E0 > , or E1  E0 < 0 (or the first iteration) 
set Fn = Pn and E1 = E0, return to Step 2.
(Case b) If 0  E1  E0    continue to Step 6.
(Step 6):
Set h[k] = s[0],
h[k+n] = s[n]/2, h[k  n] = s[n]/2 for n = 1, 2, 3, …., k
(referred to page 45)
Then h[n] is the impulse response of the designed filter.

## Slide 22
 2-G Mini-Max FIR Filter 設計時需注意的地方
62
(1) Extreme points 不要選在 transition band
Initial guess的extreme points只要注意別取在transition band裡，即能保證 converge，不同的guess會影響converge的速度但不影響結果
(2) E1 (error of the previous iteration) < E0 (present error) 時，亦不為收斂
(3) Remember to update W(Fm) and Hd(Fm) according to the locations of Fm.

## Slide 23
(4) Extreme points 判斷的規則：
(a) The local peaks or local dips that are not at boundaries must be extreme points.
63
F = 0
F = 0
err(F)
Add a zero to the outside and conclude whether the point is a local maximum or a local minimum.
(b) For boundary points (F = 0, F = 0.5)
Local peaks: err(F) > err(F + F) and err(F) > err(F  F)
Local dips: err(F) < err(F + F) and err(F) < err(F  F)

## Slide 24
64
(5) 有時，會找到多於 k+2 個 extreme points, 該如何選
(a) 優先選擇不在 boundaries 的 extreme points
(b) 其次選擇 boundary extreme points 當中 |err(F)| 較大的，
直到湊足 k+2 個 extreme points 為止
(c) 找好 extreme points 之後，要記得重新依 F 值大小排序

## Slide 25
 2-H Examples for Mini-Max FIR Filter Design
Example 1: Design a 9-length highpass filter in the mini-max sense
ideal filter: Hd(F) = 0 for 0  F < 0.25,
Hd(F) = 1 for 0.25 < F  0.5,
transition band: 0.22 < F < 0.28  = 0.001
weighting function: W(F) = 0.25 for 0  F  0.22,
W(F) = 1 for 0.28  F  0.5,
(Step 1) Since N = 9, k = (N-1)/2 = 4, k+2 = 6,
 Choose 6 extreme frequencies
(e.g., F0 = 0, F1 = 0.1, F2 = 0.2, F3 = 0.3, F4 = 0.4, F5 = 0.5)
[R(Fn) Hd(Fn)]W(Fn) = (1)n+1e, n = 0, 1, 2, 3, 4, 5.

## Slide 26
(Step 2)

## Slide 27
R(F) = 0.5120 – 0.6472cos(2F) – 0.0297cos(4F) + 0.2472cos(6F)
+ 0.0777cos(8F)
(Step 3) err(F) = [R(F) – Hd(F)]W(F)
err(F)
s [0]
s [1]
s [2]
s [3]
s [4]
W(F) = 0 for 0.22 < F < 0.28

## Slide 28
(Step 4) Extreme points:
F0 = 0, F1 = 0.125, F2 = 0.22, F3 = 0.28, F4 = 0.356, F5 = 0.5
(Step 5) E0 = Max[|err(F)|] = 0.1501, return to Step 2.
Second iteration
(Step 2) Using F0 = 0, F1 = 0.125, F2 = 0.22, F3 = 0.28, F4 = 0.356, F5 = 0.5
 s[0] = 0.5018, s[1] = –0.6341, s[2] = –0.0194, s[3] = 0.3355, s[4] = 0.1385
(Step 3) err(F) = [R(F) – Hd(F)]W(F),
(Step 4) extreme points : 0, 0.132, 0.22, 0.28, 0.336, 0.5
(Step 5) E0 = Max[|err(F)|] = 0.0951, return to Step 2.

## Slide 29
Third iteration
(Step 2), (Step 3), (Step 4), peaks : 0, 0.132, 0.22, 0.28, 0.334, 0.5
(Step 5) E0 = 0.0821, return to Step 2.
Fourth iteration
(Step 2), (Step 3) , (Step 4), peaks : 0, 0.132, 0.22, 0.28, 0.334, 0.5
(Step 5) E0 = 0.0820, E1  E0 = 0.0001  , continues to Step 6.

## Slide 30
(Step 6) From s[0] = 0.4990, s[1] = –0.6267, s[2] = –0.0203, s[3] = 0.3316, s[4] = 0.1442
h[4] = s[0] = 0.4990, h[3] = h[5] = s[1]/2 = –0.3134,
h[2] = h[6] = s[2]/2 = –0.0101, h[1] = h[7] = s[3]/2 = 0.1658,
h[0] = h[8] = s[4]/2 = 0.0721.

## Slide 31
Example 2: Design a 7-length digital filter in the mini-max sense
ideal filter: Hd(F) = 1 for 0  F < 0.24,
Hd(F) = 0 for 0.24 < F  0.5, transition band: 0.21 < F < 0.27
weighting function: W(F) = 1 for 0  F  0.21,
W(F) = 0.5 for 0.27  F  0.5,
 = 0.001
(Step 1) Since N = 7, k = (N-1)/2 = 3, k+2 = 5,  Choose 5 extreme frequencies
(e.g., F0 = 0, F1 = 0.2, F2 = 0.3, F3 = 0.4, F4 = 0.5)
Hd(F)
0
0.5
0.27
0.21
0.24

## Slide 32
(Step 2)
 s[0] = 0.5486, s[1] = 0.7215, s[2] = 0.0284, s[3] = -0.2472, e = -0.0514
Hd(F)
R(F)

## Slide 33
After Step 2,
(Step 3) err(F)
(Step 4) extreme points: 0.1217, 0.21, 0.27, 0.3698, 0.5.
(Step 5) E0 = Max[|err(F)|] = 0.2341, return to Step 2.
Iteration | 1 | 2 | 3 | 4 | 5 | 6
Max[¦err(F)¦] | 0.2341 | 0.3848 | 0.1685 | 0.1496 | 0.1493 | 0.1493

## Slide 34
After 7 times of iteration
s[0] = 0.4243, s[1] = 0.7559, s[2] = -0.0676, s[3] = -0.2619, e = 0.1493
(Step 6):
h[3] = 0.4243, h[2] = h[4] = s[1]/2 = 0.3780,
h[1] = h[5] = s[2]/2 = -0.0338,
h[0] = h[6] = s[3]/2 = -0.1309, h[n] = 0 for n < 0 and n > 6

## Slide 35
附錄二：Spectrum Analysis for Sampled Signals
Basic rule：把間隔由 1 換成 fs /N where fs = 1/ t
已知 x[n] 是由一個 continuous signal y(t) 取樣而得
x[n] = y(nt)
DFT: FT:
Q: x[n] 的 DFT 和 y(t) 的 Fourier transform 之間有什麼關係？
(學信號處理的人一定要會的基本常識)
(Very important)

## Slide 36
fs = 1/ t
for m  N/2
for m > N/2
(1)
(2)
0 fs/2 fs
0 N/2 N
frequency
m:
(2)
(1)
The DFT output has the period of N
If the sampling frequency is fs, the FT output has the period of fs
FT
DFT

## Slide 37
Proof：
用 t = nt, f = mf 代入
當
i.e.,

## Slide 38
Example：已知
y(t) = (2t)2 for 0  t  1
如何用 DFT 來正確的畫出 y(t) 的頻譜？
y(t) = (4－2t)2 for 1  t  2
取樣間隔： t = 0.1
x[n] = y(n t) for 0  n  20

## Slide 39
(Step 1) Perform the DFT for x[n]
x[n] = y(n t) for 0  n  20
N = 21

## Slide 40
(Step 2-1)
for m  N/2
for m > N/2
In this example,
(Step 2-2)
y(t) 的頻譜