## Slide 1
 2-L Frequency Sampling Method
 Frequency Sampling 基本精神：
若 Hd(f) 是 desired filter 的 discrete-time Fourier transform
R(f) 是 r[n] = h[n+P] 的 discrete-time Fourier transform
filter 的點數為 N, k = (N − 1)/2
要求
for m = 0, 1, 2, 3, ……, N − 1
fs : sampling frequency
若以 normalized frequency F = f/fs表示
for m = 0, 1, 2, 3, ……, N − 1
假設 designed filter h[n] 的區間為 n  [0 , N−1]
(see page 110)
Hd(f) = Hd(f+fs)
remember:

## Slide 2
References：
L. R. Rabiner and B. Gold, Theory and Application of Digital Signal Processing, Prentice-Hall, N. J., 1975.
B. Gold and K. Jordan, “A note on digital filter synthesis,” Proc. IEEE, vol. 56, no. 10, pp. 1717-1718, 1969.
L. R. Rabiner and R. W. Schafer, “Recursive and nonrecursive realizations of digital filters designed by frequency sampling techniques,” IEEE Trans. Audio and Electroacoust., vol. 19, no. 3, pp. 200-207. Sept. 1971.

## Slide 3
設計方法：
換句話說，r1[n] 是 Hd(m/N) 的 inverse discrete Fourier transform (IDFT)
n = 0, 1, …., N−1
Step 2
Step 3 When N is odd
for n = 0, 1, …., k
for n = -k, -k+1, …., −1
k = (N −1)/2
h[n] = r[n − k ]
注意： r[n] 的區間為 n  [−(N −1)/2, (N −1)/2]
k = (N −1)/2
Step 4
Step 1
Sampling
for m = 0, 1, 2, 3, ……, N − 1

## Slide 4
Proof:
注意，若 R(F)是 r[n] 的 discrete-time Fourier transform
又由於 r1[n] 是 Hd(m/N) 的 inverse discrete Fourier transform (IDFT)
所以
when
(We apply the fact where
when
)

## Slide 5
Example:
N = 17
Hd(F) = 1 for -0.25 < F < 0.25,
Hd(F) = 0 for -0.5 < F < -0.25, 0.25 < F < 0.5
F=1/N
F=2/N
x
(Step 1)
[ 1 , 1 , 1 , 1 , 1 , 0 , 0 , 0 , 0 , 0 , 0 , 0 , 0 , 1 , 1 , 1 , 1 ]

## Slide 6
r1[n] = ifft([1, 1, 1, 1, 1, 0, 0, 0, 0, 0, 0, 0, 0, 1, 1, 1, 1]
= [0.529 0.319 -0.030 -0.107 0.032 0.066 -0.035 -0.049 0.040
0.040 -0.049 -0.035 0.066 0.032 -0.107 -0.030 0.319]
n = 0 ~ 16
r [n] = [0.040 -0.049 -0.035 0.066 0.032 -0.107 -0.030 0.319 0.529
0.319 -0.030 -0.107 0.032 0.066 -0.035 -0.049 0.040]
n = −8 ~ 8
若我們希望所設計出來的 filter h[n] 有值的區域為 n  [0, 16]
h[n] = r[n − 8 ]
= [0.040 -0.049 -0.035 0.066 0.032 -0.107 -0.030 0.319 0.529
0.319 -0.030 -0.107 0.032 0.066 -0.035 -0.049 0.040]
n = 0 ~ 16
(Step 2)
(Step 3)
(Step 4)

## Slide 7
(Step 2)
(Step 3)
(Step 4)

## Slide 8
 The approximation error tends to be highest around the transition band
and smaller in the passband and stopband regions.
R(F)在sample frequency 等於Hd(F)
Error 非 equal-ripple
Frequency Response in terms of R(F)
(r[n] is from Step 3)

## Slide 9
Error is larger at the edge

## Slide 11
討論：
(1) Frequency sampling 的方法頗為簡單且直觀，
但得出來的 filter 不為 optimal
(2) Ripple 大小變化的情形，介於 MSE 和 Minimax 之間
(3) 可以用設定 transition band 的方式，來減少 passband 和 stopband 的 ripple。(In transition band, R(m/N)  Hd(m/N)).
然而，如何設定 transition band R(m/N) 的值，讓 passband 和 stopband 的
ripple 變為最小 ……… 需要作 linear programming。
(運算時間不少)

## Slide 12
 2-M 三種 FIR Digital Filter 設計方法的比較
 以效果而論
 以設計方法而論
 以方法的限制而論
MSE :
Minimax :
frequency sampling :
MSE :
Minimax :
frequency sampling :
MSE :
Minimax :
frequency sampling :

## Slide 13
The 4th Method for the FIR Filter Design?
Q: Why do we not apply the method?
x[n]
DFT
X[m]
Y[m] = X[m]H[m]
H[m] = 1 for passband
H[m] = 0 for stopband
IDFT
y[n]

## Slide 14
(1) 使用 FFT
 2-N Implementation of the FIR Filter
y[n] = x[n]  h[n]
convolution
(2) 直接作 summation 即可
(3) Sectioned FFT
y[n] = IFFT[ FFT{x[n]} FFT{h[n]} ]

## Slide 15
(2) 直接作 summation
y[n] = h[0]x[n] + h[1]x[n−1] + ….. + h[N −2]x[n−N+2] + h[N −1]x[n−N+1]
y[n] = x[n]  h[n]
假設 h[n] = 0 for n < 0 and n  N
 若 h[n] = h[N−1−n] (even symmetric), N 為odd
y[n] = h[0](x[n] + x[n−N+1]) + h[1](x[n−1] + x[n−N+2])
+ ….. + h[k−1](x[n−k+1] + x[n−N+k]) + h[k] x[n−k]
k = (N − 1)/2

## Slide 16
3. Theories about IIR Filters
3-A Minimum-Phase Filter
 FIR filter: The length of the impulse response is finite
usually linear phase (i.e., even or odd impulse response)
always stable
 IIR filter: (i) May be unstable
(ii) The length of the impulse response is infinite.
(Question): Is the implementation also a problem?
Advantages of the IIR filter:

## Slide 17
References
 A. Antoniou, Digital Filters: Analysis and Design, McGraw-Hill, New York, 1979.
 T. W. Parks and C. S. Burrus, Digital Filter Design, John Wiley, New York, 1989.
 O. Herrmann and W. Schussler, ‘Design of nonrecursive digital filters with minimum phase,’ Elec. Lett., vol. 6, no. 11, pp. 329-330, 1970.
 C. M. Rader and B. Gold, ‘Digital filter design techniques in the frequency domain,’ Proc. IEEE, vol. 55, pp. 149-171, Feb. 1967.
R. W. Hamming, Digital Filters, Prentice-Hall, Englewood Cliffs, NJ, 1988.
F. W. Isen, DSP for MATLAB and LabVIEW, Morgan & Claypool Publishers, 2009.

## Slide 18
 IIR filter: The length of the impulse response is infinite.
 try to make the energy concentrating on the region near to n = 0
.  try to make both the forward and the inverse transforms stable
using the minimum phase filter.
(All the poles and all the zeros are within the unit circle.)

## Slide 19
Z transform
H(z) can be expressed as
p1, p2, p3, ….. , pS : poles z1, z2, z3, ….. , zR : zeros
 Stable filter: All the poles are within the unit circle.
 Minimum phase filter: All the poles and all the zeros are within the unit circle. i.e., |ps|  1 and |zr|  1
If any pole falls outside the unit circle (|ps| > 1 ), then the impulse response of the filter is not convergent.

## Slide 20
If R  S, Q(z -1) is a polynomial of z -1 with degree R–S.
If R < S, Q(z -1) =0.
for n = 1, 2, 3, 4, …..
If |ps| < 1,
If |ps| > 1,
inverse Z transform

## Slide 21
Therefore,
where
for s = 1, 2, ….., S
FIR filter
geometric series

## Slide 22
unit circle |z| = 1
Im(z)
Re(z)
poles zeros
Thus, the minimum phase filter is stable and causal.
The inverse of the minimum phase filter is stable and causal.

## Slide 23
Suppose that z2 is not within the unit circle, |z2|> 1
The upper bar means conjugation.
 3-B Converting an IIR Filter into a Minimum Phase Filter
不影響amplitude

## Slide 24
In fact, if (see page 28), then H(z) and H1(z) only differ in phase,
(proof):
when
 We call the filter whose amplitude response is always 1 as the all-pass filter.
is an all-pass filter
(單位圓上)
 One can also use the similar way to move poles from the outside of the unit circle into the inside of the unit circle.

## Slide 25
Any stable IIR filter can be expressed as a cascade of the
minimum phase filter and an all-pass filter.
H(z) :IIR filter, Hmp(z): minimum phase filter, Hap(z): allpass filter
stable and causal IIR filter
=
minimum phase filter
all-pass filter

## Slide 26
Example:
conjugates with
h[n], h1[n] are the impulse response of the two filters H(z) and H1(z)
(origin)
(minimum phase)

## Slide 27
 3-C The Meaning of Minimum Phase
when n < 0
when n  0
br[0] = 1, br[1] = zr ,
br[0] = 0 otherwise
Another important advantage of the minimum phase filter：
The energy concentrating on the region near to n = 0.
n=0
n=1

## Slide 28
Phase is related to delay
discrete time
Fourier transform
Minimum phase  Minimum delay
The multiplications in the Z domain (frequency domain) are equivalent to the convolutions in the time domain, so we could analyze each term individually in the previous page!!

## Slide 29
(Question): How about the case of |pn| = 1 or |zn| = 1?

## Slide 30
135
附錄四：查資料的方法
(1) Google 學術搜尋 (不可以不知道)
網址： http://scholar.google.com.tw/
(太重要了，不可以不知道) 只要任何的書籍或論文，在網路上有電子版，都可以用這個功能查得到
輸入關鍵字，或標題、作者
再按「搜尋」，就可找到想要的資料
註：由於版權，大部分的論文必需要在學校上網才可以下載

## Slide 31
136
按搜尋之後將出現相關文章
可限定要找的文章的刊登時間
若要引用這篇論文，可點選此按鈕，會出現三種不同格式的引用方式
點選後，可找到該學術文章的原始出處和相關的電子檔

## Slide 32
137
(2) 尋找 IEEE 的論文
http://ieeexplore.ieee.org/Xplore/guesthome.jsp
(6) 傳統方法：去圖書館找資料
台大圖書館首頁 http://www.lib.ntu.edu.tw/
或者去 http://www.lib.ntu.edu.tw/tulips
(3) Google
(4) Wikipedia
(5) 數學的百科網站
http://eqworld.ipmnet.ru/index.htm
有多個 tables，以及對數學定理的介紹
註：除非你是 IEEE Member，否則必需要在學校上網，才可以下載到 IEEE 論文的電子檔

## Slide 33
138
(7) 查詢其他圖書館有沒有我要找的期刊
台大圖書館首頁
其他聯合目錄
全國期刊聯合目錄資料庫
台大圖書館首頁
館際合作
如果發現其他圖書館有想要找的期刊，可以申請「館際合作」，請台大圖書館幫忙獲取所需要的論文的影印版
「台大圖書館首頁」
「其他圖書館」
(8) 查詢其他圖書館有沒有我要找的書
「台大圖書館首頁」
「電子書」
或「免費電子書」
(9) 找尋電子書

## Slide 34
139
http://www.cetd.com.tw/ec/index.aspx
(10) 中文電子學位論文服務
可以查到多個碩博士論文 (尤其是 2006年以後的碩博士論文) 的電子版
(12) 有了相當基礎之後，再閱讀 journal papers
(以 Paper Title， Abstract， 以及其他 Papers 對這篇文章的描述，
來判斷這篇 journal papers 應該詳讀或大略了解即可)
(11) 想要對一個東西作入門但較深入的了解:
看書會比看 journal papers 或 Wikipedia 適宜
如果實在沒有適合的書籍，可以看 “review”， “survey” ，或 “tutorial” 性質的論文

## Slide 35
(13) 積分查詢網站：http://integrals.wolfram.com/index.jsp
(14) 可以查詢數學公式的工具書 (Handbooks)
M. R. Spiegel, Mathematical Handbook of Formulas and Tables, McGraw-Hill, 3rd Ed., New York, 2009. (已經有電子版)
M. Abramowitz and I. A. Stegun, Handbook of Mathematical Functions, with Formula, Graphs and Mathematical Tables, Dover Publication, New York, 1965.
A. Jeffrey, Handbook of Mathematical Formulas and Integrals, Academic Press, San Diego, 2000.