## Slide 1
Homework 1 (Due: March 20th)
(1) Design a Mini-max lowpass FIR filter such that (40 scores)
 Filter length = 17,  Sampling frequency fs = 6000Hz,
 Pass Band 0~1200Hz  Transition band: 1200~1500 Hz,
 Weighting function: W(F) = 1 for passband, W(F) = 0.6 for stop band .
 Set  = 0.0001 in Step 5.
0 Hz
1200 Hz
1350 Hz
1500 Hz
※ The code should be handed out by NTUCool, too.
Show (a) the frequency response, (b) the impulse response h[n], and
(c) the maximal error for each iteration.

## Slide 2
(2) How do we implement y[n] = x[n] *(0.8nu[n] + 0.5nu[n]) efficiently where * means convolution and u[n] is the unit step function? (10 scores)
(3) (a) What are the two main advantages of the Fourier transform (FT)? (b) What are the two main problems to implement the FT? (10 scores)
(5) Why (a) the step invariance method and (b) the bilinear transform can reduce or avoid the aliasing effect in IIR filter design? (10 scores)
(4) Suppose that x[n] = y(0.002n) and the length of x[n] is 2000. If X[m] is the FFT of x[n], which frequencies do (a) X[200] and (b) X[1600] correspond to? (10 scores)
(6) (a) Which of the following filters are usually even? (b) Which of the following filters are usually odd? (i) Notch filter; (ii) highpass filter; (iii) edge detector; (iv) integral; (v) differentiation 4 times; (vi) particle filter; (vii) matched filter. (10 scores)

## Slide 3
(7) Use the MSE method to design the 7-point FIR filter that approximates the lowpass filter of Hd(F) = 1 for |F| < 0.25 and Hd(F) = 0 for 0.25 < |F| < 0.5. (15 scores)
(Extra): Answer the questions according to your student ID number.
(ended with 0, 1, 2, 3, 5, 6, 7, 8)